## Slide 1: SAP-1
Let’s go ..

## Slide 2: Introduction
The Simple-As-Possible (SAP)-1 computer is a very basic model of a microprocessor explained by Albert Paul Malvino.
The SAP-1 design contains the basic necessities for a functional Microprocessor.
Its primary purpose is to develop a basic understanding of how a microprocessor works, interacts with memory and other parts of the system like input and output.
The instruction set is very limited and is simple.

## Slide 3: What SAP-1 contain?
Output
Register
RAM
16*8
MAR
Adder/
Sub
RegB
PC
IR
AC
Controller

## Slide 4: 1-Program Counter(PC)
The program is stored at the beginning of the memory with the first instruction at binary address 0000 the second instruction at address 0001, the third at address 0010, and so on.
The program counter, which is part of the control unit, counts from 0000 to 1111.
Its job is to send to the memory the address of the next instruction to be fetched and executed.

## Slide 5: 2-Inputs and MAR (Memory Address Register)
During a computer run, the address in PC is latched into Memory Address Register (MAR).

## Slide 6: 3-RAM
The program code to be executed and data for SAP-1 computer is stored here.
During a computer run, the RAM receives 4-bit addresses from MAR and a read operation is performed. Hence, the instruction or data word stored in RAM is placed on the W bus for use by some other part of the computer.
It is asynchronous RAM, which means that the output data is available as soon as valid address and control signal are applied.

## Slide 7: 4-Instruction Register(IR)
IR contains the instruction (composed of OPCODE+ADDRESS) to be executed by SAP1 computer.

## Slide 8: 5-Controller-Sequencer
It generates the control signals for each block so that actions occur in desired sequence. CLK signal is used to synchronize the overall operation of the SAP1 computer.
A 12-bit word comes out of the Controller-Sequencer block. This control word determines how the registers will react to the next positive CLK edge.

## Slide 9: 6-Accumulator(AC)
It is a 8-bit buffer register that stores intermediate results during a computer run.
It is always one of the operands of ADD, SUB and OUT instructions.

## Slide 10: 7-ALU
It is a 2's complement adder-subtractor.
This module is asynchronous (unclocked), which means that its contents can change as soon as the input words change.

## Slide 11: 8-B-register
It is 8-bit buffer register which is primarily used to hold the other operand (one operand is always accumulator) of mathematical operations.
9-Output Register
This registers hold the output of OUT instruction.

## Slide 12: SAP-1 architecture
Instructions
DATA

## Slide 13: SAP-1 Instructions and Instruction Cycle

## Slide 14
Control Unit

## Slide 15: Instruction Fetch and Execute

## Slide 16: Control Unit Design

## Slide 17: Control Unit Design Cont.

## Slide 18
Let’s Take a Example

## Slide 19
0000
0000
0000 1001
0001
0000 1001
0000
1001
0000 0001
0000 0001
0001
0001 1010
0001 1010
0001
1010
0011
0x02
0x02
0x03
0x03
0x03
0x06
0x06
0x04
0x02
0x02
0x02
1111 1111
1111 1111
1111
Computer Halted
0x03
0x06
0x02

## Slide 20
Difference between SAP 1 and Basic Computer

## Slide 21
SAP 1
Basic Computer

## Slide 22
SAP-1 & SAP-2

## Slide 23
SAP 1
SAP-2

## Slide 24
SAP-1 & MIPS

## Slide 25
SAP 1
MIPS

## Slide 26: Let’s go to the Code

## Slide 27: Thanks